Scope of Work – Leesville OMV:

Contractor shall provide all labor and materials in order to complete the interior repairs of damages caused during Hurricane Laura and the Ice Storm of February 2021 to the Leesville Office of Motor Vehicles (OMV) for the Louisiana Department of Public Safety (DPS).

Contractor shall:

- Furnish all labor, equipment and supplies necessary for the completion of the stated repairs.

- Move out, then reset all contents as required to complete project.

- Disconnect/reconnect system wiring as needed in order to make repairs to building (mechanical room).

- Mask and cover all surfaces and fixtures to protect from paint spillage, drippage, etc.

- Coordinate work required after regular business hours (8:00 a.m. to 4:30 p.m.) with Ellen Tyree, office manager.  Any work hour changes must also be coordinated and approved by office manager.

- Provide job-site storage, with delivery and pick-up, as required to hold supplies and/or materials.

- Dispose of all materials and debris resulting from the repairs and provide for removal of same.

Repairs:

- Contractor shall replace missing 5/8” drywall with appropriate sized material in three locations.

  - Estimated total Square Feet (SF) = 186.5 SF

| Location | Estimated SF |
| --- | --- |
| OMV Employee Work Area | 18.0 |
| Hallway | 116.5 |
| Mechanical Room | 52.0 |

- All drywall patches that are new and previously replaced shall be prepared by contractor for painting to blend smoothly with existing wall surfaces in 10 areas. Contractor shall float or tape the seams, either is acceptable, and apply texturing to match existing wall surface.

  - Estimated area for application of texturing = 274.5 SF.

| Location | Estimated SF |
| --- | --- |
| OMV Employee Work Area | 18.0 |
| Lobby/Waiting Room | 54.0 |
| Hallway | 116.5 |
| Mechanical Room | 52.0 |
| Janitor’s Closet | 12.0 |
| Men’s Restroom | 6.0 |
| Women’s Restroom | 6.0 |
| LANG Recruiter Office | 4.0 |
| Game Warden Office | 2.0 |
| “Side 2” Breakroom | 4.0 |

- Contractor shall seal stained surface area with a latex based stain blocker – one coat.

  - Estimated total Square Feet (SF) = 32 SF

| Location | Estimated SF |
| --- | --- |
| Lobby/Waiting Room | 32.0 |

- Contractor shall paint all walls in listed areas with two coats of Low VOC Latex paint, eggshell finish in white.  Floors and adjacent surfaces not being painted are to be taped/masked for protection.

  - Estimated total Square Feet (SF) = 5,174.8 SF

| Location | Estimated SF |
| --- | --- |
| OMV Employee Work Area | 1,268.0 |
| Lobby/Waiting Room | 1,148.0 |
| Hallway | 310.7 |
| Mechanical Room | 277.3 |
| Janitor’s Closet | 192.0 |
| Men’s Restroom | 368.0 |
| Women’s Restroom | 496.1 |
| LANG Recruiter Office | 309.3 |
| Game Warden Office | 309.3 |
| “Side 2” Breakroom | 496.1 |

- Contractor shall paint ceiling in OMV Employee Work Area and Lobby with one coat of Interior Ceiling White Flat paint. All surfaces, items in painting area are to be protected by the contractor during work.

  - Estimated total Square Feet (SF) = 2300 SF

- Contractor shall remove and replace 16 LF of high-grade plastic laminate counter facing approximately 40” high. This is to be 1/8” formica or equal matte finish in speckled gray color.

- Install replacement VCT Tile in rear entryway where removed in standard commercial white color.

- Install medium gray 4” Rubber or Vinyl cove base molding in all listed areas.

  - Estimated total Liner Feet (LF) = 408 LF

| Location | Estimated LF |
| --- | --- |
| OMV Employee Work Area | 41.0 |
| Lobby/Waiting Room | 102.0 |
| Hallway | 39.0 |
| Janitor’s Closet | 24.0 |
| Men’s Restroom | 41.0 |
| Women’s Restroom | 41.0 |
| LANG Recruiter Office | 39.0 |
| Game Warden Office | 19.0 |
| “Side 2” Breakroom | 62.0 |

Terms and Conditions:

- Vendor representatives must follow all policy and procedures while performing work at the facility.